## Slide 1: Dissipation element analysis
Christian Boehme
Institute for Combustion Technology RWTH Aachen University

## Slide 2: DE theory
Overview
Regime diagram

## Slide 3: Dissipation element theory 1/3
Peters and Wang https://linkinghub.elsevier.com/retrieve/pii/S1631072106001173
Goal: search for random geometrical elements in turbulence (represent turbulent “eddies”)
  Subdivide the flow into finite size regions
    Subdivision follows the structure of the flow
    Independent from an arbitrary numerical mesh
  Method:
    Trajectories normal to iso-surfaces (on a scalar field)
    Identify minimum and maximum points (local extreme points)
    Finite elements between minimum and maximum points are referred to as “dissipation elements”
    Within this region, the scalar filed is monotonic

## Slide 4: Dissipation element theory 2/3
Peters and Wang https://linkinghub.elsevier.com/retrieve/pii/S1631072106001173
Statistical properties of dissipation elements (DE)
  Linear distance between minimum and maximum
  Absolute of scalar difference at these points
  Scalar gradient
Mechanism of extreme points generation
  Same order of magnitude for diffusion velocity and local convective velocity leads to the generation of extreme points
  Convective motion alone is unable to generate extreme points
  Extreme points are generated at scales of the Obukhov-Corrsin length
DEs: Tool for describing & investigating the effect of turbulence & diffusive transport on scalar fields.
DEs: Space-filling objects which subdivide the entire turbulent scalar field into smaller sub-units.
Notes: Obukhov-Corrsin length: Kolmogarov velocity v_k=(eps*r)^(1/3) equals diffusion velocity v_c=D/r

## Slide 5: Dissipation element theory 3/3
Peters and Wang https://linkinghub.elsevier.com/retrieve/pii/S1631072106001173
Probability density of elements with length l
Postulate: time evolution of extremal points exhibits several stochastic features
  Generation of new extremal points resulting from eddy turnover of Obukhov-Corrsin eddies
    “cutting process”
  Merging of two extremal points that are at a very small distance to each other. Leads to disappearance of these points, resulting in a reconnection of the adjacent elements
    “reconnection process”

## Slide 6: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
What was done?
  DE analysis applied to mixture fraction field of DNS of non-premixed jet flames with different jet Reynolds numbers and stoichiometric mixture fractions
  Comparison of statistics of DE parameters of non-premixed flames to non-reacting jets
What was found out?
  Universality of the normalized length distribution of the DE observed in non-reacting cases also holds true for the reacting flows
  Effects of combustion on the scalar difference in DEs
    Diminish as the Reynolds number and the fuel dilution increases
  New regime diagram for non-premixed combustion is introduced
    DE parameters for a local classification of the turbulent flame surface
    Flamelet-like zones / fine-scale mixing zones / burning zone / non-burning zone
Denker2020

## Slide 7: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
Observations:
  DEs are intersected by the flame
  Size of DEs increases toward the flame
    Increased diffusivity caused by the heat release & mean relative velocity in the cross-stream direction
    Intersection area depends on the DE orientation
  DE tend to be elongated tube-like structures
Mixture fraction Z is used as scalar field – non-premixed combustion
  Provides most meaningful scales for the investigation of turbulent/chemistry interaction
DE analysis of mixture fraction field
Mirrored mixture fraction Z field
Denker2020

## Slide 8: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
Influence of small scale turbulence in combustion
  Normally: local reaction layer thickness compared to turbulent length scale
  Non-premixed combustion: width of reaction layer changes locally with mixture fraction gradient
  Comparison of scales between the scalar difference with the reaction layer thickness
    Comparison in mixture fraction field
    = length in Z-space (flamelet like solutions exist)
    Gradient trajectories used to identify DEs are identical to the physical coordinates of flamelets
      DEs as groupings of flamelet solutions
  Flame thickness in non-premixed flames varies greatly with the mixture fraction gradient
    Introduction of second parameter to characterize DE:
    Its square is related to the scalar dissipation rate
Denker2020

## Slide 9: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
(1) global maximum of jPDF
  diffusive drift of the extreme points leading to an annihilation of small DEs
(2) probability of ramp-cliff structures
  structures are linked to external and internal intermittency and manifest themselves in very steep gradients of the scalar followed by a very gradual decent.
(3) physical mechanism of splitting and reconnection of DEs
jPDF reactive cases => see Denker et al.
General observations:
  High Reynolds numbers: jPDF resembles non-reactive case
  Low Reynolds numbers jPDFs are different to the non-reactive case
    poor mixing in the reactive regions of the flow
Denker2020
Non-reactive case I
(1)
(2)
(3)

## Slide 10: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
Categorization of combustion regimes based on DE parameters
DE parameter based regime diagram
  Gradient
    Boundary: quenching gradient
  Scalar difference
    Boundary: threshold value Z-space - below this value no coherent 1-D flame structure can be formed
Regimes:
  Burning flamelets
  Large scale extinction
  Fine scale mixing
  Broken reaction zones
Denker2020
Notes: Threshold in Z-space: Equation (2) Niemietz et al.

## Slide 11: DE analysis of non-premixed jet flames
Denker et al. https://www.cambridge.org/core/product/identifier/S0022112020007168/type/journal_article
Regimes:
  Burning flamelets
    Regions of the flames should adhere to the classical steady flamelet model
  Large scale extinction
    “large scale”: characteristic scale of the extinction-inducing event, which is large compared to the scale indicated by the local DE
    Large cliff-ramp structures with significant strain; Large-scale extinct regions such as flame holes
    Extinction corresponds to the low Damköhler type extinction caused by eddies of integral scale size
  Fine scale mixing
    Very short flamelet solutions; questionable if chemical reactions can be sustained
    Rapid splitting and reconnection
    Flame structure should not exist (comp. homogeneous reactor); intense turbulent advection is the dominant transport mechanism
  Broken reaction zones
    small-scale extinction zones due to locally high turbulence activity
    type of extinction corresponds to a high Karlovitz-type effect - eddies of the size of the Kolmogorov-scale transport radicals out of the inner reaction zone
Denker2020

## Slide 12: Prediction of non-premixed combustion regimes in DI-compression engines
Niemietz et al. https://linkinghub.elsevier.com/retrieve/pii/S1540748924002505
What was done?
  Methodology to link DNS and RANS
    Three-ponged approach combines universal scaling relations of turbulence and chemistry from DNS data with the mean values from RANS and 1D detailed chemistry calculations
    Test case: direct injection compression ignition engine
    Local probabilities of each regime based on universal DE-statistics
      i.e. for the flamelet regime:
What was found out?
  Applied framework to predict non-premixed combustion regimes in RANS based on DNS, 1D detailed chemistry & CFD
  For the largest part (~90%), combustion took place in the flamelet regime
    Confirms suitability of the flamelet model
Local combustion regime distribution:
Local probability:

## Slide 13: Spray combustion and dissipation elements; a novel analysis approach
Bode et al. “Spray combustion and dissipation elements: a novel analysis approach”
What was done?
  DE applied to DNS data of spray combustion
  Analysis of temperature and mixture fraction field
  Spray combustion: DE applied to combustion and liquid evaporation
    Prior ignition and after ignition
What was found out?
  Application of DE to spray combustion
  Analysis of combustion modeling approaches based on DE
    DE statistics of ignited spray similar to homogeneous isotropic turbulence
    DE statistic before ignition is different due to another DE length scale corresponding to the droplet distribution
      Droplet length scale is no longer characteristic after ignition
Notes: Used “in-house trajectory search code” (DESC) => access this code/ITV-code?

## Slide 14: Project
Idea

## Slide 15: Idea
Determine regime diagram for ..
  Check if flamelet solution is applicable
Further:
  Calculate regime diagram for two-time steps to see the evolution in the regime-diagram
    0.5 (ignition end + small flame)
    0.65 (evolved flame)
  Consumption speed
    Reactants at Zst front (reaction rates)
    Two different time steps